## Slide 1: Wireless Router Setup
An Introduction to Wireless Router Setups

## Slide 2: Wireless Routing
What was life like before wireless?
Would the Internet be as popular without wireless?

## Slide 3: Why Use Wireless?
Convenient
Networking all the time
Not limited to the number of ports

## Slide 4: RF Basics
Wireless uses specific frequencies
The frequencies are measured in Hertz (Hz)
A single Hertz is one cycle per second
Cycle = measure of wave from start to repeat of start position
Measuring from the top of one wave to the top of the next
Modern wireless is measured in Gigahertz (GHz)
1GHz = 1,000,000,000 Hz

## Slide 5: RF Basics - Modern Frequencies
2.4 uses the range of 2.400 GHz - 2.4835 GHz
5.0 uses the range of 5.150 GHz - 5.825 GHz
What are the 2 most common frequencies in use today?

## Slide 6: RF Basics - Spread Spectrum
2.4 uses the range of 2.400 GHz - 2.4835 GHz
5.0 uses the range of 5.150 GHz - 5.825 GHz
To achieve bandwidth, we spread the data across frequencies
This is known as Spread Spectrum
Spread Spectrum used 79 channels, each 1MHz wide (slow speed)

## Slide 7: RF Basics - Direct Sequence Spread Spectrum
With DSSS, channels are 22 MHz each
This provides 14 channels
Only 3 do not have overlap (1, 6, and 11)
Wireless routers in close proximity should be on different channels

## Slide 8: Wireless Router Location
Location, location, location
Easier for signal to fall down floors than to rise up floors
Keep away from other devices like microwaves
Keep away from portable phones
Keep away from wireless speakers

## Slide 9: Exercises
Connect the same laptop to the wireless router using a cable
Set the laptop IP address to be 192.168.1.2
Connect a laptop to the big screen TV at your table(s)
Turn on wireless router
Open browser on laptop and visit 192.168.1.1
You should be at the wireless router config wizard screen
Click the skip wizard button

## Slide 10: The 802.11 Standard
802.11 Ratified in 1997. It was 1-2Mbps in the 2.4 GHz range.
802.11a Ratified in 1999. Up to 54Mbps in the 5 GHz band.
802.11b Ratified in 1999 as well. DSSS.
802.11g Ratified in 2004. 54Mbps in the 2.4 band.
802.11n and 802.11ac
n was ratified in 2009 with data rates over 100Mbps. Includes MIMO ops.
ac was ratified in 2014. Provides data rates in the Gbps range.

## Slide 11: The Service Set Identifier
The SSID is nothing more than the name of the network
Change the SSID, NEVER leave it the default
You can hide the SSID if you want (not advertised)

## Slide 12: Wireless Router Admin Password
The admin password authenticate you into the router
This admin password gives you admin/root privileges
Should we change this from the default?

## Slide 13: Wireless Authentication
WEP was the original standard (deprecated)
Use WPA2 with AES encryption (don’t use TKIP)
Always require your wireless users to provide a password

## Slide 14: MAC Address Lists
Blacklist - block the MAC addresses you list
Can be painful to manage
Whitelist - only allow the MAC addresses you list

## Slide 15: Update the Firmware of the Wireless Router
“Flashing” the firmware will update the router
If something goes wrong in process, usually very bad results
Just like laptops and desktops, routers need updating

## Slide 16: Exercises
Make sure you are on the proper channel (Wireless/General)
Make sure you are using WPA2 and AES (Wireless/General)
Configure a 2.4 network (SSID name and passphrase)
Enable the Firewall and DoS protection (Firewall)
Have the other laptops connect to your new wireless network

## Slide 17: Exercises
Only list the laptops at your table
Try to connect to the new wireless network with a phone
Create a whitelist for MAC addresses (Wireless/MAC Filter)

## Slide 18: Exercises
Share your guest network name and password with next table
Try to connect a laptop at your table with the guest network at the next table
Create a guest network